## Slide 1: My Background
Flying RC sailplanes since 1976
First competition 1977 US Nationals, placed 2nd
Only pilot to win world champion for both FAI recognized soaring disciplines
FAI world record holder for declared distance to a goal (141 miles, set in 1988)
A “lifer” in the sport

## Slide 2: Finding and Recognizing Thermals
Joe Wurts

## Slide 3: Topics of Discussion
Thermal Theory
Application
Thermal Sources
Non-Thermal Lift

## Slide 4: Thermal Theory - Basics
Basic definition: lighter than the surrounding air
Thermal shapes
  Column
  Bubble
  Disorganized blob
  Streets

## Slide 5: Thermal Theory - Climate Influences
Humidity
Ground moisture
Lapse rate
Inversion height
Cloudiness

## Slide 6: Thermal Theory - Characteristics
Feeds from warm air near the ground
Drifts with the wind
Attraction to other thermals
Thermal aspect ratio

## Slide 7: Application - Clues to Finding Thermals
Detecting thermal inflow
  Inflow signs
  Wind lulls, changes
  Wind shifts
    Do not confuse with thermal inflow
Ground signs
  Look for the “third vector”
What you feel
(Wind + Inflow)
Wind
Inflow
Wind
Thermal Inflow

## Slide 8: Application - The Third Vector
Mental vector math = Direction to thermal
What to look for
  Temporary changes in the wind
    Direction
    Speed
Wind + Inflow
= What you feel
Wind
Inflow
Thermal
Wind

## Slide 9: Application - The Third Vector
Mental vector math = Direction to thermal
What you feel
Wind
Inflow
Thermal Inflow
The wind if there
was no thermal
If you are
standing here...
The wind + thermal inflow =
the wind that you feel
(The third vector)
Thermal

## Slide 10: Application - The Third Vector
Mental vector math = Direction to thermal
Wind
Inflow
What you feel
Do the math to derive the direction to the thermal
Note the wind speed and direction that you feel
Subtract the basic wind
The result is the change caused by the thermal
Wind
Inflow
(this points to the thermal)

## Slide 11: Application - Practical Guidelines
Sharply defined upwind edge
Diffuse downwind edge
Convergence zones
Angled streets
Wind

## Slide 12: Application - Perspective Challenges
Confusion between range and altitude
Elevation angle confusion
Wind

## Slide 13: Application - Hints on Recentering
Turn tighter in the stronger lift
Constantly reevaluate on each circle
Be wary of subconscious upwind drift
Effects of horizontal wind shear
Wind
Wind Speed
Altitude

## Slide 14: Morning Conditions - Inversions
Wind Speed
Altitude
Typical wind profile with altitude
Wind Speed
Altitude
Temperature
Inversion
Wind profile low level inversion
Temperature
Altitude
Temperature
Inversion
Temperature profile low level inversion

## Slide 15: Thermal Sources
Heating sources
  Drier ground
  Radiation sources
Terrain influences
  Tree lines
  Hills
Wind

## Slide 16: Non-Thermal Lift
Wave
  Conditions necessary
  When likely
Shear line
Hydraulic wave
Dynamic soaring

## Slide 17: Optimizing Your Aircraft Set-up
Joe Wurts

## Slide 18: Topics of Discussion
Philosophy
The Mechanical Aspects
Mixing
Flight Modes

## Slide 19: Philosophy
Optimizing the aircraft efficiency and performance
  Minimizing drag
  Getting the most capability
Eliminating the “cross-talk” in inputs
  Goal is coordinated flight without difficulty
Ease of Control
  Ease of flying = more performance realized

## Slide 20: The Mechanical Aspects
Servo installation
  Install servos to get straight pushrods
Servo linkage and throws
  Stiff and tight linkage without drag
Wiring suggestions
Note servo arm angle forward
and control arm angle aft,
produces progressive mechanical
differential - good for ailerons

## Slide 21: Mixing - Roll Axis
Goal - Coordinated roll w/o separate rudder
Aileron to Flap mixing
  Increases roll efficiency (I use Flap = 40% Ail)
Differential vs Rudder coupling
  Best help in setup - slope on a light day
  Slow speed vs high speed
  Dependence on aircraft configuration
  Typical 1.5:1 to 2.5:1 differential

## Slide 22: Mixing - Pitch Axis
Primary mix is Elevator to Camber
  Camber should be even across the wing
  If possible, use an inverse exponential mix
    More camber mix initially
  A good start is full up mixes to 10° camber
    Highly dependent on airfoil usage
Vee Tails
  More down throw than up for a symmetric pitch response

## Slide 23: Mixing - Yaw Axis
Vee Tails
  Rudder mix typically needs “reverse differential”
    The more “vertical”, the more “reverse differential”
  Less efficient than a cross-tail
Mostly covered in “roll axis”
Reverse
Differential

## Slide 24: Flight Modes
I use four flight modes
  Launch
  Speed
  Cruise
  Thermal
Each mode has a different, ail>rud mix, differential, camber and elevator preset, as well as control throw setting

## Slide 25: Flight Modes - Launch
Camber preset
  15° to 30° camber preset (full span)
  Dependent on airfoil usage
Elevator preset
  Highly dependent on towhook position
  Neutral to slight amount of up is best
Aileron to Rudder mixing
  More is better
Up to 100% aileron differential

## Slide 26: Flight Modes - Thermal
Camber presets or adjustments
  I use flight mode presets, with adjustable slide for fine tuning
Camber to (Ail to Rud) gain adjustments
  More camber should give more Ail to Rud gain
Elevator to Camber mix
  Keep this mix (many people do not)
Aileron to Rudder mix
  Go to a higher rate for slow speeds
Reduced Aileron and Elevator throws

## Slide 27: Flight Modes - Speed
Reflex Camber settings (fallacies)
Elevator to Camber mix
  Use a bit more (higher loads cause “blow-back”)
  More if using reflex camber preset
Aileron to Rudder mix
  Minimize this
Differential changes
  Possibly a reduction is warranted

## Slide 28: Flight Modes - Landing
Flap to Elevator mix
  Highly non-linear after 45° flap
Flap to Aileron (crow)
  I use about 10° up aileron
Aileron to Rudder mix
  Add some to suit
Differential adjustments
  Typically a bit more is needed
Goal of crow/ail>rud/diff is slightly proverse yaw response with a roll input
Flap Throw
Pitch up is caused by
downwash on the elevator
0°
90°

## Slide 29: Launch Optimization
Joe Wurts

## Slide 30: Topics of Discussion
Launch Modelling Program
Aircraft Set-Up for Launch
The Throw
The Zoom
Winch/Line Optimization
System Losses
Steering on Tow
Crosswind Launching
Circle (Weave) Towing

## Slide 31: Launch Modelling Program
Baseline Assumptions
  Straight tows only (no weaving)
  Power on 100%
  Default data:
      Weight 96 oz
      Aspect Ratio 12.5
      Wing Area 7.0 ft2
      Throwing Line Ten 50 lb.
      Launch Cl 0.80
      Wind Velocity 10 ft/sec
      Zoom Point 75 deg up from turnaround
      Winch Drum Dia 3.5 inches
0
10
0
200
300
400
500
600
700
0
200
400
600
800
100
0
Typical Launch

## Slide 32: Aircraft Set-Up for Launch
Full-span launch camber typically 20 to 25°
Elevator pre-set
  Most fliers have too little up pre-set and/or towhook too far forward
More Aileron to Rudder mix
Tow hook position (very important)
  Optimum needs just a little up pre-set

## Slide 33: The Throw
In general, as hard as possible with as much tension as possible
  Exception - circle towing
Should be more vertical

## Slide 34: Effect of Zoom Position
Zoom start point from 50° to 95°, measured from the turnaround
  Zoom early in the wind (30 ft/sec wind optimum is 60°)

## Slide 35: How Deep to Zoom
It is better to be too shallow than too deep
  The pullout is very expensive in energy
  Deeper = faster (and draggier)
Start your pullout with 10 to 20 lbs tension
  Best with a slight “pop” of the chute
Go to nearly vertical quickly (hard pull-out)
  Fast transition from high drag to low drag

## Slide 36: Winch Optimization
Use the correct drum size for the conditions
Use the “right” resistive material
  Try Constantin
Minimize losses in the system
  Heavy duty selenoid
  Large, short cabling

## Slide 37: Line Optimization
Line size
  Use the minimum size that wil not break
Stretch characteristics
  Optimum line for wind is different than no wind
  Line that has some plasticity is good for “weaving” in the wind
Rebound characteristics
  Some lines do not spring back quickly

## Slide 38: System Losses
The biggest is line drag in the air
  Minimum line size for the conditions
  Maximize Cl capability on tow
Parachute drag is important
  Minimize parachute and shroud size
  Try “double-hooking”
Aircraft set-up can have a factor (Trim Cl)

## Slide 39: Steering on Tow
Being on tow is similar to flying very slowly (high Cl)
You should use a lot of rudder along with a little aileron
When there is little tension, the plane might need some down elevator
Note line tension
is behind the CG

## Slide 40: Crosswind Launching
The optimum launch is from straight downwind of the turnaround
  As soon as is practical after the throw, turn the aircraft to get downwind of the turnaround
  Then turn back up the tow to finish the launch
A side benefit is that you can better gauge your zoom dive/pullout

## Slide 41: Circle (Weave) Towing
The basic idea is to use the energy of the wind instead of the winch motor
  Line that stays off of the drum helps your launch height
  Tension is everything
Use weaving to build tension and gain altitude